## Slide 1
Strength of Materials
Module 7
(Column & Pressure Vessels)
Dr. G.Venkatachalam
Professor / SMEC
VIT Chennai Campus
Chennai

## Slide 2
Beam
Bar
Column

## Slide 4
Column – structure subjected to compression
Pole vault stick when athlete grounds it
I – moment of inertia;
A – area of cross section

## Slide 5
Why such divisions are required?

## Slide 6
Buckling load (Euler’s formula) – for different end conditions – He says “if this criteria is met, column will buckle. Buckling is an undesirable phenomena.

## Slide 7
Comparison of Euler & experiment
Euler prediction
Experimental values
Euler formula is good only for long columns. How short column & intermediate columns are dealt??

## Slide 8
FR – Rankine load;
FC – Compressive load;
FE – Euler’s load
Short column to buckle – high buckling load is required.
Long column to compress – high compressive load is required.

## Slide 9
For intermediate column, both compression & buckling effects are included.
Suitable changes are to be made according to the end conditions in FE substitution.

## Slide 10
Tutorials

## Slide 11
Advantages of using hollow circular column over solid circular column.

## Slide 13
Euler formula prediction (1.125 kN) is higher than the Rankine formula (0.5 kN) – L/K ratio must be checked.

## Slide 14
Pressure Vessels

## Slide 15
Why do we need to classify thin cylinder and thick cylinder???

## Slide 16
Due to critical σL, cylinder is broken in to 2 (or more) cylinders.
Due to critical σh, cylinder is broken in to 2 (or more) hemispheres.

## Slide 20
ΣF = 0 is used; Force due to fluid pressure = force due to internal resistance
Force due to fluid pressure
Force due to internal resistance
P – fluid pressure

## Slide 21
Same approach mentioned in previous slide is extended here
Inferences??

## Slide 23
Bi-axial state of strain – to find Δd & ΔL

## Slide 24
To find Δd & ΔL – why it is required to be found out??

## Slide 29
A boiler is subjected to an internal steam pressure of 2 N/mm2. The thickness of boiler plate is 2.0 cm and permissible tensile stress is 120 N/mm2. Find out the maximum diameter, when the efficiency of longitudinal joint is 90 % and circumference joint is 40 %.

## Slide 30
Here there is only hoop stress

## Slide 34
5. 150 kN;
6. 4290 m

## Slide 35
Thank You